## Slide 1: Development of High Resolution & Large Pad Anode Readout for MPGDs
Kondo Gnanvo
EIC Weekly Meeting, June 01, 2020

## Slide 2
Principe of large pads readout with high spatial resolution capabilities
2 large pads (1 cm2) share the initial charges: position from COG ⇨ expected similar or better performances in spatial resolution as X/Y strips with 100 pads instead of 512 for a XY readout
DLC layer
Dielectric: Kapton foil
Dielectric: Kapton foil
Dielectric: Kapton foil
Dielectric: Kapton foil
GND
DLC layer to evacuate the charges to the ground
Initial electron clouds size from triple GEM amplification will hit one pad of .6125 cm (average cluster size = 3 for a standard COMPASS XY R/O)
Readout pad 1 cm
Transfer pad 0.5 cm
Transfer pad 0.25 cm
Transfer pad 0.125 cm
Transfer pad 0.6125 cm
Stack of pad layers (5 layers for UVa prototype): 50 µm Kapton with 5 µm Cu pads ⇨ The pad size doubles (area × 4) from one layer to the layer underneath
Pad are arranged in space so that 2 neighboring pads of a given layers always partially share the same area with 2 neighboring pads on the layer underneath
Initial charges shared from one layer to the layer underneath through capacitive coupling (geometrical charge spread)
  Regardless size of bottom layer pads, at least always 2 pads see hits from initial charge cloud hits at least 2 pads of top layer
Only bottom pad layer is read out (readout layer) all the other layers on top participates only on the capacitive coupling charge spread (capacitive layers)
  Spatial resolution performances dictated in first order by the top layer pad size, independent of the bottom pad size
DLC layer on top of the first pad layer is mostly to evacuated the charges from the amplification but could contribute to the initial charge spread
  However DLC charge spread requires pad response function ⇨ so might requires some optimization to minimize its contribution to the charge sharing

## Slide 3
UVa prototype with triple GEM
Five layers Large Pad Anode Readout:
Standard CERN triple-GEM Active area: 90 mm × 90 mm
Top layer pad pitch: 0.625 mm × 0.625 mm with 0.1 mm inter-pad
Bottom pad pitch (readout pad): 10 mm × 10 mm with 0.1 mm inter-pad
DLC layer with surface resistivity 10 - 20 MOhm
1 Panasonic connector
DLC layer
DLC ground ring
Back side with pad traces to the connector

## Slide 4
Preliminary results with x-ray: 2D hit reconstruction
Average pad hit occupancy: 6 pad (3 in x × 2 in y) ⇨ average beam size spread: 3 cm × 2 cm
Average size of the reconstructed beam: 4 mm x 3 mm ⇨ strip occupancy / spot size ratio = 50
Uniform distribution of the reconstructed hits: 2D histogram with 25 µm × 25 µm bin size
  No specific pattern that could correlate with the pad RO geometry
  Excellent spatial resolution performances expected with this simple geometry and pad size specific
Simple 2D center of gravity algorithm is applied for reconstructing the hit position

## Slide 5
Cluster size pad distribution
Preliminary results : ADC and cluster size vs. divider HV
ADC (blue) 2D cluster size (red) vs. HV
Average cluster size > 4 at 4.3 kV with x-ray
  Here 4.3 kV with x-Ray equivalent to 3.65 kV with standard GEM because the DLC layer increases the divider resistance from 5.5 Mohm to 6.5 Mohm
Average cluster size = 8 for HV = 4.6 kV which seems to be to optimal operating voltage for x-Ray
Gain vs. HV curve good fit with exponential function
ADC distribution from cosmic data: Landau function

## Slide 6
Ideas for R&D and Optimization
Some challenges specific with this concepts
Minimizing the material thickness of such RO: Adding these layers considerably increases the material thickness of the detector
  Exploring the idea with Chromium pads to considerably reduce the overall thickness (will be part of my 2020 funding request for eRD6)
Need to minimizing the capacitance noise of the large size pads: In first order, spatial resolution not limited by the readout layer pad size However
  However large pad ⇨ large capacitance noise that will degrades signal to noise and therefore the spatial resolution performance
  Some R&D ideas under consideration to significantly reduce the capacitance noise (discussing these ideas with Rui)
Next studies in the pipeline
Study the detector response linearity ⇨ (with the BNL x-ray scan facility for example)
Evaluate the spatial resolution performance with MIP at Fermilab Test beam in Spring 2021
Study impact of strip inter pad gap on the readout performances (linearity, spatial resolution etc …)
Some obvious applications in our field of Tracking detector R&D
Applying the same idea charge sharing through capacitive coupling to other type of readout geometry
  X/Y strip, zig-zag, U/V strips, non-square pads …
This concept will work perfectly well in moderate rate environment like for EIC tracking system
  uRWELL prototype with such large ad readout (will be part of my 2020 funding request for eRD6)
  Ultimately, one would want to study the performance of such readout with cylindrical shape MPGD detectors…
  TPC GEM readout with large pad will considerably reduce the number of channel count without penalty on the spatial resolution performance
Will this approach also work for the various MPGD-based PID detectors under development with eRD6?
  Silvia Hybrid MPGDs High Momentum RICH or SBU short length GEM-RICH?

## Slide 7
BACKUP

## Slide 8
Spatial resolution performances basically depends on how many pads from top layers have hits
Typically, charges from a standard (3-2-2-2-) triple-GEM will hit on average 3 COMPASS X-Y (400 µm pitch) strips,
So with DLC layer contribution, top layer pad size of 0.6125 µm will always have at least two pads with hit on average in each direction
  Meaning at least 4 pads (x and y direction) on average with hit on top layers ⇨ so expect an average number of pad on the readout layer > 4
Illustration here in one direction only
GND
2 pad hits
2 pad hits
2 pad hits
2 pad hits
2 pad hits
Principe of large pads readout with high spatial resolution capabilities

## Slide 9
GND
3 pad hits
2 pad hits
2 pad hits
2 pad hits
2 pad hits
Principe of large pads readout with high spatial resolution capabilities
Spatial resolution performances basically depends on how many pads from top layers have hits
Typically, charges from a standard (3-2-2-2-) triple-GEM will hit on average 3 COMPASS X-Y (400 µm pitch) strips,
So with DLC layer contribution, top layer pad size of 0.6125 µm will always have at least two pads with hit on average in each direction
  Meaning at least 4 pads (x and y direction) on average with hit on top layers ⇨ so expect an average number of pad on the readout layer > 4
Illustration here in one direction only

## Slide 10
GND
3 pad hits
3 pad hits
2 pad hits
2 pad hits
3 pad hits
Principe of large pads readout with high spatial resolution capabilities
Spatial resolution performances basically depends on how many pads from top layers have hits
Typically, charges from a standard (3-2-2-2-) triple-GEM will hit on average 3 COMPASS X-Y (400 µm pitch) strips,
So with DLC layer contribution, top layer pad size of 0.6125 µm will always have at least two pads with hit on average in each direction
  Meaning at least 4 pads (x and y direction) on average with hit on top layers ⇨ so expect an average number of pad on the readout layer > 4
Illustration here in one direction only

## Slide 11
GND
3 pad hits
3 pad hits
3 pad hits
2 pad hits
3 pad hits
Principe of large pads readout with high spatial resolution capabilities
Spatial resolution performances basically depends on how many pads from top layers have hits
Typically, charges from a standard (3-2-2-2-) triple-GEM will hit on average 3 COMPASS X-Y (400 µm pitch) strips,
So with DLC layer contribution, top layer pad size of 0.6125 µm will always have at least two pads with hit on average in each direction
  Meaning at least 4 pads (x and y direction) on average with hit on top layers ⇨ so expect an average number of pad on the readout layer > 4
Illustration here in one direction only

## Slide 12
GND
3 pad hits
3 pad hits
3 pad hits
2 pad hits
3 pad hits
Principe of large pads readout with high spatial resolution capabilities
Spatial resolution performances basically depends on how many pads from top layers have hits
Typically, charges from a standard (3-2-2-2-) triple-GEM will hit on average 3 COMPASS X-Y (400 µm pitch) strips,
So with DLC layer contribution, top layer pad size of 0.6125 µm will always have at least two pads with hit on average in each direction
  Meaning at least 4 pads (x and y direction) on average with hit on top layers ⇨ so expect an average number of pad on the readout layer > 4
Illustration here in one direction only

## Slide 13
GND
3 pad hits
3 pad hits
3 pad hits
3 pad hits
3 pad hits
Principe of large pads readout with high spatial resolution capabilities
Spatial resolution performances basically depends on how many pads from top layers have hits
Typically, charges from a standard (3-2-2-2-) triple-GEM will hit on average 3 COMPASS X-Y (400 µm pitch) strips,
So with DLC layer contribution, top layer pad size of 0.6125 µm will always have at least two pads with hit on average in each direction
  Meaning at least 4 pads (x and y direction) on average with hit on top layers ⇨ so expect an average number of pad on the readout layer > 4
Illustration here in one direction only

## Slide 14
Preliminary results with cosmics: ADC and cluster size vs. divider HV